## Slide 1: AI Sandboxing for 6G Ecosystems From Digital Twin to Autonomous Networks
Michael Dieudonne
Keysight Technologies
September 2026
Notes: AI-native 6G networks require more than advanced AI algorithms. They depend on trusted, high-quality, and continuously updated data. This presentation introduces a data-centric framework that combines digital twins, cloud-native observability, open telemetry, and data management to create consistent and AI-ready datasets from live, emulated, and synthetic sources. Digital twins provide a safe environment for data generation and AI validation, while observability frameworks deliver real-time network insights. Together, these capabilities enable the training, testing, and deployment of AI applications such as anomaly detection, root cause analysis, energy optimization, and autonomous network control, establishing the trusted data foundation needed for autonomous 6G networks.

## Slide 2: Why Data Matters for AI-native 6G
A 6G‑native AI system is only as good as the data it receives
To build trustworthy AI models, we must verify not only the AI but also the system generating the data and the data itself. You need to verify the system, the AI, and the data.
Instagram, Nov 6th 2025
The three fundamental questions are:
Where do the data come from? An AI‑native 6G workflow requires multiple complementary data sources. No single source is enough.
How do you ensure this is “good data”? “Good data” means accurate, clean, consistent, and usable.
How do you ensure the data is up‑to‑date? AI for 6G must continuously adapt as the network evolves (mobility, load, weather, interference, new deployments).
If not… it may rain fish!
© Keysight Technologies, Inc.
Notes: Why Data Matters for AI‑Native 6G
In 6G, AI will be embedded in every layer of the network—but the performance of that AI depends entirely on the quality of the data it receives.
Before we can trust AI models, we must verify not only the AI itself, but also the system producing the data and the data pipeline behind it. If any of these elements fail, the AI will make wrong decisions—even if the model is perfect.
The three fundamental questions are:
First, Where do the data come from?
AI-native 6G requires multiple complementary data sources—RAN, Core, Edge, NTN, and Digital Twin. No single source is sufficient.
Second, How do we ensure the data is “good”?
Good data must be accurate, consistent, clean, and fit for training or inference. Bad data produces bad AI outcomes.
Third, How do we ensure the data stays up to date?
6G networks evolve rapidly: mobility, load fluctuations, interference, weather, and new deployments constantly change the network’s state. AI must continuously adapt to remain valid.
Why this matters
If we don’t ensure trustworthy data, AI systems will confidently make incorrect conclusions—just like the viral video shown here, where AI misinterpreted a fake scenario as real. This illustrates how easily AI can be misled when data is wrong or unverified.
Core message
Reliable AI for 6G requires end-to-end verification of the system, the AI models, and the data pipeline. This is the foundation for the rest of the architecture we will walk through.

## Slide 3
Video posted on Instagram & Youtube on Nov 6th 2025.
© Keysight Technologies, Inc.
Google Search, June 8th, 2026.
Google Search, July 28th, 2026.
Gemini AI will finally acknowledge that this is a fake news and explain how the AI get fooled ! Only since July 2026
Notes: “Here I want to show how generative AI is now capable of fabricating entire events with convincing realism. On the left, you see a video circulating widely on Instagram and later YouTube in November 2025, supposedly showing ‘fish raining from the sky’ in Georgia. On the right, you see a Google search result that appears to validate the event.
But none of this is real. The video is AI‑generated, and the search results were manipulated or fabricated. This illustrates how GenAI can create a complete, believable information ecosystem around a fake event — video, imagery, captions, even search‑engine‑looking pages.
The lesson: AI will confidently tell you something is true, even when it never happened. This is why verifiable data and trusted visibility sources matter more than ever.

## Slide 4: Data pollution via Adversarial Machine Learning techniques
5G/6G governed by AI… but can we trust the data sets training the models?
Deep learning technologies (DNNs) has enabled high-accuracy AI systems to be widely deployed in real-world applications, but their vulnerability to adversarial attacks poses significant security risks, making robustness a critical challenge.
https://doi.org/10.3390/electronics9111957
Adding small, well-crafted perturbations to the original image leads DNNs into making incorrect predictions, and not by just a bit!
© Keysight Technologies, Inc.
Notes: Adversarial machine learning is a growing threat in the AI and machine learning research community. The most common reason is to cause a malfunction in a machine learning model; an adversarial attack might entail presenting a model with inaccurate or misrepresentative data as its training or introducing maliciously designed data to deceive an already trained m
Split the image animation..

## Slide 5: What if you train a Neural receiver with incomplete data?
Published paper on 5G Beam selection for a supervised, Multi Class Classification CNN model.
Dataset was made public as part of the publication.
Takeaway: TEST YOUR AI DATASET!
Lack of meaningful training data creates wrong results
Klautau, Aldebaro, et al. "5G MIMO data for machine learning: Application to beam-selection using deep learning." 2018 Information Theory and Applications Workshop (ITA). IEEE, 2018.
https://github.com/lasseufpa/5gm-beam-selection/tree/master/classification
(Transmitter Antenna, Receiver Antenna)
Actual: There are 61 classes in the labels, but the dataset is imbalanced with the top-1 class occupying 61.25% of the labels in the train set respectively, and the top-3 classes occupy 80.83%..
Feedback:
(1) Collect more data points for classes with less data points.
(2) Under sample classes with many data points, or over sample classes with less data points.
© Keysight Technologies, Inc.

## Slide 6: The Four Steps of AI-RAN
Intelligent Anomaly
Detection & Fake basestation det.
Building the Data Pipeline that Powers AI‑Native 6G
The first operational capability of AI-native 6G
Data
Management
Network
Insights
Digital Twin
The Safe Sandbox for AI
Turn Data in Understanding
Turning raw data into curated AI-ready dataset
Customer AI-RAN application
© Keysight Technologies, Inc.
Notes: In this slide, we introduce the end‑to‑end flow that transforms raw network data into actionable intelligence for 6G. This is the “backbone story” for how Keysight enables AI‑native networks.
1. Digital Twin
“Let me start with the first building block: the Digital Twin.
This is where we create a high‑fidelity, virtual replica of the real network. It allows us to test configurations, explore extreme scenarios, and generate synthetic data in a safe, repeatable environment.
The Digital Twin is essential because it provides the training and validation space for AI models before they ever touch the live network.”
2. Network Insights
“Once we have the Digital Twin, the next step is to make the network observable.
With cloud‑native observability and O‑RAN telemetry, we can collect consistent KPIs across RAN, Core, and Cloud. This is where we begin to understand real behavior through per‑UE metrics, E2/O1/A1 signals, and cross‑layer correlation.
Network insights turn raw data into meaningful intelligence.”
3. Data Management
“The third layer is data management.
Here we merge three types of data: real network data, Digital Twin data, and emulated test data.
The role of this step is to ensure quality, consistency, lineage, and scalability so that the resulting datasets are AI‑ready. This is the point where data becomes usable for training, benchmarking, and validating AI and ML models.”
4. Intelligent Anomaly Detection & Root Cause Analysis
“And all three steps lead to the first real operational capability of an AI‑native 6G network: intelligent anomaly detection and automated root‑cause analysis.
At this stage, the AI learns what ‘normal’ looks like and detects deviations early. We can reproduce anomalies inside the Digital Twin to understand them, correlate causes across RAN, core, and cloud, and present clear decision paths to the operator.
This is how we move from observability toward autonomous 6G operations.”
“Together, these four steps form a unified pipeline that takes us from raw data to trustworthy AI and ultimately to automated, intelligent 6G networks.”

## Slide 7: Digital Twin The Safe Sandbox for 6G AI

## Slide 8: Digital Twin – The Safe Sandbox for 6G AI
Creation of the wireless environment digital twin
Making of the Digital Twin
Digital Twin creation
© Keysight Technologies, Inc.
Notes: “This slide illustrates how we build a realistic wireless‑environment Digital Twin — the safe sandbox where 6G AI can learn, test, and fail without harming the real network.
On the left, you see the data‑collection phase: we capture the physical environment using drone imagery. The mapping exercise requires planning and time, and challenges are not unusual, like the time in which our drone was attacked by seagulls that clearly do not appreciate any ‘intrusion” in their airspace.
On the right, you see the resulting 3D digital replica. This model is then enriched with accurate electromagnetic properties so we can simulate signals, mobility, interference, and edge cases that are impossible or too costly to reproduce in the field.
This Digital Twin becomes the foundation for training and validating 6G AI models safely, repeatedly, and at scale.”

## Slide 9: Digital Twin – The Safe Sandbox for 6G AI
Digital Twin Innovation for 6G and AI-Driven mMIMO
Virtualization – Generate a calibrated digital twin from field measurement
Channel Data Generation – Generate and export site-specific channel data
Beamforming prediction – Predict and optimize the network’s beamforming
KPI Verification – Compare over-the-air performance with Keysight emulated testbed
© Keysight Technologies, Inc.
1
2
3
4
Notes: This slide shows how we build an RF Digital Twin from real field measurements to support AI‑native 6G research. We start by capturing site‑specific data from the physical environment, which is then virtualized inside the RaySim RF Digital Twin. From this calibrated model, we generate realistic channel data and predict mMIMO beamforming performance using a customer network simulator. Next, the same scenarios are replayed through PROPSIM and the UXM 5G Network Emulator to validate the results over the air. This end‑to‑end workflow lets us compare predicted and real performance, ensuring that AI models trained on the Digital Twin will behave reliably in the live network.

## Slide 10: Digital Twin – The Safe Sandbox for 6G AI
From Sensing Target and channel modeling to real time emulation
ISAC Modeling
Real-World ISAC Deployed in a Network
3GPP TR 38.901 Rel‑19 aligned lab solution
Unified ISAC modeling and real-time emulation solution
Scalable platform from early sensing R&D to full system validation
Sensing
TRP
Sensing
UE
Bistatic Sensing
example
Sensing Signal
Communication Signal
Sensing
Target
Real-Time ISAC Emulation
Validated ISAC algorithms and devices
1
2
3
S8808A ISAC Channel Emulation Toolset
S8808A ISAC Channel Emulation Toolset
ISAC Use Case scenario modeling
© Keysight Technologies, Inc.
Notes: “This slide shows how we take an ISAC use case from pure simulation into a full real‑time emulation environment. We start with ISAC modeling, where we build the sensing scenarios and generate channel conditions in a lab setup aligned with 3GPP TR 38.901. Next, we move into real‑time ISAC emulation using the S8800A toolset, where algorithms and devices can be tested against realistic dynamic conditions. Finally, those same sensing behaviors are deployed into a network‑scale environment, where we validate performance in a real‑world scenario. This workflow gives us a unified, scalable platform to develop, benchmark, and verify ISAC algorithms before they go into live 6G systems.”

## Slide 11: Digital Twin – The Safe Sandbox for 6G AI
ISAC Digital Twin with AI Object Recognition
© Keysight Technologies, Inc.

## Slide 12: Network Insights Turning Data+Twin into Understanding

## Slide 13: Network Insights – Cloud-Native RAN Observability
Enabling AI RAN, intent driven, intelligent, automated decision-making across the RAN
Today’s observability tools are costly, limited, and vendor‑locked. Mobile Operator get a report every 5 minutes!
There are almost no valid datasets available with enough resolution; DT is still only synthetic data! Good but not real!
RAN observability remains complex and expensive, with traditional tools difficult to deploy and manage.
O‑RAN disaggregation and open telemetry enables standardized cloud‑native observability.
Keysight provides the observability framework!
Observability supplies the trusted, real‑time data AI requires to detect issues, optimize the network, and prove ROI
Real network
Notes: Network Insights: Observability Unlocks AI ROI
AI can only optimize what it can see. Today’s observability and visibility tools are fragmented, expensive, and often vendor‑locked. With O‑RAN telemetry and cloud‑native observability, operators finally get standardized access to real‑time RAN data. Keysight enhances this with analytics and Digital Twin environments that turn this raw data into actionable insights. Observability gives AI the trusted, real‑time data it needs to detect issues early, optimize network performance, and prove ROI.

## Slide 14: AI-RAN Deep Telemetry Private Network PoC
Demo of a live AI RAN deep telemetry system at EUCNC 2026
© Keysight Technologies, Inc.

## Slide 15: AI-RAN Deep Telemetry Private Network
RAN Data
Workload Data
Energy Data
RAN Data Lake – Observability Framework
FlexRIC
Grafana
influxdb
O-CU ID = 411
telegraf
O-CU ID = 400
O-DU ID = 1
O-DU ID = 2
O-DU ID = 3
RAN KPIs
telegraf
F1 Interface
N2(AMF) & N3(UPF)
Interface Taps
Internet
Emulated Cells
Live Cells
E1
E2
Live Cell ID’s
L1 = 6733824
L2 = 6733825
L3 = 6733826
PLMN ID = 99950
Emulated Cell ID’s
E1 = 6553601
E2 = 6553602
PLMN ID = 99950
Fronthaul 7.2x Interface
LoadCore
COT Servers
VNFs deployed
in k8s pods
Tenerife
Ethernet Backhaul
L1
L2
L3
telegraf
Vision X Packet Broker
VisionWorks
RuSIM
telegraf
Server A: 10.20.40.1
Server B: 10.20.3.1
Server C: 10.20.85.1
Server D: 10.20.2.1
Server E: 10.20.4.1
N4(SMF) & N11(PDU)
Interface Taps
Server F: 10.20.4.1
Simplified Flow Diagram
© Keysight Technologies, Inc.
Notes: https://6g-sandbox2.eu/metrics
https://analytics.vwx1.tsa-sa.net/auth?use_local
Victoria
PLMN Victoria 999 29
PLMN 6G-SANDBOX2 999 50
Hierro – 10.20.20.30
Grancanaria – 10.20.30.1
Tenerife – 10.20.4.1
Lapalma – 10.20.2.1
Fuerteventra – 10.20.85.1
Lanzarote – 10.20.40.1
N4 Interface
Session establishment, modification, and deletion in the UPF
Traffic steering and routing rules
QoS enforcement policies
Forwarding rules (PDRs, FARs, QERs, etc.)
Usage reporting (e.g., for charging/analytics)
N11 Interface
PDU session lifecycle management
  Session establishment
  Modification
  Release
SMF selection by AMF
Session context transfer
Policy/control signaling related to sessions

## Slide 16: Network KPI Dashboards
© Keysight Technologies, Inc.

## Slide 17: O-RAN UE KPIs
UE-side service, radio quality, and data-session indicators collected during trial
© Keysight Technologies, Inc.

## Slide 18: Observed O-RAN Anomalies Under Stress Conditions
Signaling Storms and Handover-Induced O-DU Stress
Suspected Memory Leak: Increasing handover activity correlates with growing O-DU memory usage, followed by an apparent O-DU recovery event.
Signaling Storm Experiment: UEs entered flight mode and later reconnected, resulting in a temporary gap in UE measurement data.
© Keysight Technologies, Inc.
Notes: The figure shows UE-level O-RAN KPIs during a signaling storm experiment. At the highlighted interval, all UE-related measurements, including CQI, Timing Advance, RSRP, SNR, and throughput, disappear simultaneously. This behavior is consistent with UEs entering flight mode or disconnecting from the network, resulting in the temporary absence of active UE measurements. Normal KPI reporting resumes once the UEs reconnect and re-establish network connectivity.
The figure illustrates the evolution of O-DU memory consumption and DU handover activity over time. Memory usage increases steadily alongside the cumulative number of DU handovers, suggesting a potential relationship between handover processing and resource consumption. At approximately 18:00, memory utilization drops abruptly while handover counters reset, indicating a probable O-DU container or application restart. The observed behavior is consistent with a resource exhaustion scenario, potentially caused by a memory leak associated with prolonged handover activity, although additional software logs are required to confirm the root cause.

## Slide 19: Data Management Where real, emulated, and synthetic data converge

## Slide 20: Data Management: AI RAN Solution Workflow
Model validation
Model deployment
(Lab, Digital Twin, or Live)
  Model design & development
  Model training
  Model evaluation
  Varied data sources
  Data curation
Benchmarking & Explainability
Data
Management
Model Training & Evaluation
Deployed AI Model
AI-ready Training Data
Candidate
AI Model
© Keysight Technologies, Inc.
Notes: The AI RAN workflow, as illustrated in the slide, follows a continuous cycle linking data management, model training and evaluation, and benchmarking and explainability. It begins with data management, where diverse network data sources are collected, curated, and prepared for analysis. This data feeds into the model training and evaluation phase, where AI models are designed, trained, and tested to address specific RAN optimization tasks such as scheduling, beamforming, or anomaly detection.
The resulting models are then subjected to benchmarking and explainability, where their performance, reliability, and interpretability are validated through deployment in lab, digital twin, or live environments. Insights from this phase feed back into data management, enabling continuous improvement of AI models and ensuring that the AI RAN system evolves dynamically with real-world network conditions.

## Slide 21: Keysight AI RAN Solution Workflow– Detailed View
Data Sources
Problem Definition
Model
Deployment
Model Design
and Development
From
User
Live Network
Benchmarking & Explainability
Data Store
RAN Performance Benchmarking
Data
Management
Data Curation
AI Model Validation
(in RAN Context)
Model Training & Evaluation
AI Model Training
AI Model Benchmarking
(in isolation)
AI Model Evaluation
Pass
From Keysight
Emulated Testbeds
Network
Digital Twin
Pass
Fail
Data Import
Continuous Monitoring & Improvement
© Keysight Technologies, Inc.
Notes: “This slide shows the full end‑to‑end workflow for developing and validating AI models in the RAN using live data, Digital Twins, and emulated testbeds. We begin with problem definition and model design, fed by data from the live network and from Keysight’s Digital Twin and emulation platforms. All data flows through the Data Management layer, where it is imported, curated, and stored for training. Models are then trained, evaluated, and benchmarked—first in isolation, and then in a realistic RAN context using the Digital Twin. If a model fails validation, it loops back for redesign; if it passes, it moves to deployment and continuous monitoring. This closed‑loop workflow ensures trustworthy, repeatable AI development and smooth integration into live 5G and future 6G networks.”

## Slide 22: Merging Data Sources
Real live data, emulated data, synthetic data
Live Networks
Emulated Testbeds
Keysight Solutions & Customer DUTs
Network Digital Twins
High Scale
High Fidelity
Network
Digital Twin
Emulated Testbeds
Live Network
© Keysight Technologies, Inc.
Notes: “This slide shows how we merge three complementary data sources to build trustworthy AI for the RAN. First, we use Network Digital Twins to generate high‑scale, high‑fidelity synthetic data and to reproduce controlled scenarios that may be rare or risky in the real network. Second, Emulated Testbeds provide repeatable lab conditions for validating algorithms and device behavior with Keysight’s tools or customer DUTs. Third, Live Networks supply real‑world measurements that anchor all models in reality. All three sources feed a unified AI development platform, where data is curated, stored, and used for training, benchmarking, and evaluating AI/ML models. By combining synthetic, emulated, and live data, we ensure models are both robust and deployment‑ready.”

## Slide 23: Intelligent Anomaly Detection & Root Cause Analysis The first real step toward an autonomous 6G network

## Slide 24: Intelligent Anomaly Detection – First 6G AI Capability
Keysight Automated RCA and Visualization Platform
The First Monetizable 6G AI Use Case: Automated RCA
AI learns “normal behavior” and detects anomalies in RAN & core.
Digital Twin enables safe training on known faults before deployment.
Keysight provides:
  Anomaly modeling
  Root‑cause analysis tools
  Visualization platforms (UE‑centric, geographic views
© Keysight Technologies, Inc.
Keysight solutions produces Immediate commercial value:
reduces OPEX and improves network reliability
Notes: Intelligent Anomaly Detection: First 6G AI Capability
One of the first real AI capabilities operators can deploy is automated anomaly detection. AI learns what ‘normal’ looks like and quickly identifies when the network deviates. Digital Twins allow operators to simulate known faults safely and use them to train models. Keysight provides anomaly models, RCA tools, and visualization platforms that allow operators to drill down into issues quickly. This brings immediate commercial value by reducing OPEX and improving reliability.

## Slide 25: Intelligent Anomaly Detection – First 6G AI Capability
Demo Video
© Keysight Technologies, Inc.

## Slide 26: Conclusions
From Digital Twin to Autonomous 6G: Key Takeaways
Digital Twin – Safe Learning & Validation High‑fidelity digital twins provide risk‑free scenario testing, synthetic data generation, and reliable AI model validation — the foundation of trustworthy 6G intelligence.
Network Insights – Full Network Visibility Cloud‑native observability and O‑RAN telemetry deliver the visibility needed to understand network behavior and drive data‑based optimization.
Data Management – AI‑Ready Data at Scale Combining live, emulated, and synthetic data ensures high‑quality, consistent, and scalable datasets for training and improving 6G AI models.
Intelligent Anomaly Detection & RCA – First 6G AI Capability Learning “normal” behavior enables early anomaly detection, Digital‑Twin‑based diagnosis, and automated root‑cause analysis across RAN, Core, and Cloud.
© Keysight Technologies, Inc.
Notes: “This slide brings together the five key takeaways from the entire presentation. First, Digital Twins give us a safe, high‑fidelity environment to test scenarios, generate synthetic data, and validate AI models before deployment. Second, Network Insights provide the observability we need — using cloud‑native tools and O‑RAN telemetry — to truly understand network behavior. Third, Data Management merges live, emulated, and synthetic data to create high‑quality, scalable datasets for training 6G AI. Fourth, Intelligent Anomaly Detection and RCA is the first concrete capability of AI‑native 6G, using the Digital Twin for diagnosis and automated root‑cause analysis. And finally, Agentic AI moves us toward fully autonomous 6G networks, enabling intent‑driven decisions and real‑time adaptation with rigorous Digital Twin testing.”

## Slide 27
Keysight uniquely spans the full AI‑RAN data generation and validation, positioning us as the essential partner for the telecom ecosystem on their path to intelligent & autonomous networks.
AI RAN Simulation Toolset
System Design
WirelessPro
MTRX/Propsim
FieldFox
NEMO
UXM
RaySim
AC/DC Power analyzers
UE&RuSIM
X-series SA/SG
WaveJudge
VisionWorks
LoadCore
Vision X Packet Broker
UXA Scope
© Keysight Technologies, Inc.

## Slide 28: References
6G DevOps: Facilitating AI and Yielding Systematic Insights in 6G Evolution
Energy-Efficient Virtualized gNB for Cloud-Native O-RAN
Efficient Resource Allocation for NextG O-RAN VNF based on Systematic Characterization
An O-RAN Digital Twin to Train AI/ML in Anomaly Detection
© Keysight Technologies, Inc.